ERROR 1:

In the “oi.h” file that is linked with all AVRDUDE programs there are constants for nearly all possible commands that can be executed.  There is a section commented as

“…// Sensor byte indices - offsets in packets 0, 5 and 6…”

These constants are not entirely correct.  I trusted some of these names in my project, but they turned out to be incorrect.  For example, I needed to check for a bump.  According to the names given to the constants I would test 0 which is SenBumpDrop.  I tested and tested until I came to the conclusion that this was incorrect.  The command I was supposed to execute was 7 which is labeled as “SenOverCh”, however it SHOULD be listed as SenBumpDrop.  The correct values were found in the Open interface manual in the Sensor Packet Membership Table on page 35 of the manual.  This is to be trusted, not necessarily all the comments in the supplied code.

ERROR 2:

The red arrows show how two pins share the same location.  This is not the case, this table is mislabeled.  This table can be found on page 32 of the command module manual.  The correct label should read “PC1 in Top Center ePort pin 2” and “PC5 in Top Center ePort pin 1”.  This is the only error I found in this table.  If there are any other incorrect listings, the correct placement of pins is found on page 31.  It is the same information listed by ePort position.