## Slide 1: iRobot Create
Sasha Popov
April 27, 2011

## Slide 2: Original Project Definition
Develop communication protocol so that two create robots can partner and cooperate activities.

## Slide 3: Initial Design
Use GPS to track the robots
Use PC as the “brains” behind the robots
Communicate via Bluetooth to control the robots

## Slide 4: Initial Equipment Limitations/ Project Evolution
Failure of the GPS due to lack of accuracy
Project Evolves:
  Create a user interface to control the robot via Bluetooth
  Use internal Robot’s readings to measure movement distances and directions
  Develop an algorithm to keep track of the robot
    Backtrack to the starting location

## Slide 5: New Focal Points
User Interface
Serial Port/Bluetooth Communication
Multi-processing
  Robot
  PC
    Multi-threading
Modified Stack for movement history

## Slide 6: Design Overview
iRobot
Internal Processor
Via Bluetooth
PC
SERIAL PORT
Threads/Log/Logic
User Interface
Request Data
Return Data
Notes: Give example of Data Request
Talk about “dumb” roomba and the brains of the PC

## Slide 7: User Interface

## Slide 8: Demo
Demo

## Slide 9: History Stack
Direction Key(back/forward/left/right)
Distance Driven
Angle Turned
Bump Sensor
Speed
1(B,F, R, L)
255
2
0
90
0
3
Drive Forward 67 mm at speed of 3 | 1 | 1
 | 2 | 0
 | 3 | 67
 | 4 | 0
 | 5 | 0
 | 6 | 0
 | 7 | 3
Turn Left 90 Degrees | 1 | 4
 | 2 | 255
 | 3 | 245
 | 4 | 255
 | 5 | 90
 | 6 | 0
 | 7 | 4
Stack Example:

## Slide 10: Extra Features of the Stack Class
Moving?
Last executed Direction?
Last Executed Command Line?
Add another command to the stack?
  Command Line == state (Drove x, Turned x, Change Speed, Sensor Bumped)
  “Buffer Commands/ Distances”- buffer the current command in progress
Size? Number of Commands
Notes: Each command line is a state of the robot
Make states smoother I “buffer” the state in progress, add 90 degrees instead of 1 degree at a time

## Slide 11: Multi-Processing
2 Asynchronous Processors
  PC
  iRobot
PC Threading
  Serial Port
    iRobot<-> PC Communication Time
    Sending Data/ Listening for Feedback
  User Interface
  Issuing Commands(Turning Right/Left)
  Lock Variable(on issuing commands to the robot)
Notes: Go through very quickly and show chart on next page

## Slide 12: Main Threads
BUMP SENSOR THREAD
Check Sensor
Wait
Loop
Right Turn /
Left Turn
Command Thread
Issue Turn
Wait To Turn x degrees
Submit Data to Log
Backtracking Thread
Execute Backtrack algorithm
Serial Port
Send Command
Spin and Listen for Result
User Interface/Main Thread

## Slide 13: Threading / Lock Variables / Turning Example
Turn Right 90 Degrees
Main Thread/
User Interface
Know When Turn Is Done
Allow To Click And Stop Turn
Turn Right Thread
Lock Out Other Threads
Issue start moving command
Loop:
  Ask for degrees turned so far
  If 90
    Add Deg. To Stack
    Stop Robot
    Release Thread Lock
Notify Main Thread That Turn Is Completed
Start The Turn Right Thread
Serial Port
Thread
Send Command
Wait For Response
Start Turning
How far did you it turn since last request?
iRobot Create
Process Command
Send Feedback
Notes: Kill thread with lock variable locked in another thread
Who stops the robot if the thread is killed half way
How far did we go?
Make sure the thread is finished so next one can start.
Reset variables of movement... Etc.

## Slide 14: Limitations
Delay between PC <-> iRobot, not accurate angles (accuracy of +- 3,4 degrees/mm)
Errors (3,4 degrees) accumulate over number of commands
  If off by 3 degrees on first turn, 2 turn could be off by as much as 6 and so on…
  Not Completely Centered Wheels (.5 inches longer in the front).
  No third source of data to correct for these errors( GPS )
Threading / Lock Variables
  Side-effects of asynchronous processing
    Hard to find and accommodate for all possible errors with so many processes happening at the same time
    “Racing conditions” on the serial port(don’t want to break up logical segments of code to and from the robot)

## Slide 15: Demo
Demo

## Slide 16: Accomplishments
Backtracking
Checks and stops on bump
Turning on the move
Multi-threading
User Interface

## Slide 17: To Do For Next Year
3rd Reference Point for the Robot
  Different GPS?
  Use another source to verify robot location/ correct for errors in reading data
Be able to coordinate two robots, even something as simple as, one drive away and the second follow

## Slide 18: Advice For Next Year
Often easier to re-write from the beginning than to understand other’s code
  Start with my basic functions (Move Forward, Backwards, Left, Right)
  At first ignore threading/stack to easily understand the basic functionality
  Use the basic commands (+ threading) as building blocks from which to build your own algorithm logic

## Slide 19: Learning and Development Process
Finding Answers:
  Google and examine sample code
    MSDN
  Build small programs to test and understand sample code
  Write my version of sample and add it to a bigger picture
CS Courses That Were Most Helpful:
  Operating Systems
  Database Modeling Project in C#
  Assembly Language (Low Level Understanding)